## Slide 1: Secrets of the Motherboard
Graham Sutherland
Security Advisory EMEAR, Cisco Advanced Services
44CON 2017

## Slide 2: Hello.
Twitter: @gsuberland
StackExchange: Polynomial
Email: gsutherl@cisco.com

## Slide 3: Where it all began
Tweets by @whitequark used with permission.

## Slide 4: Scope of this talk
Identifying security issues with modern computer hardware (treat it just like IoT devices!)
Attempts at restoring privacy, ownership, and security
Architectural failings in hardware design
Code and data persistence
Secure hardware re-use
Amusing findings along the way
Why this talk?
  Many talks focus on single issue(s)
  Nobody (afaik) has done a wide-coverage "state of play" talk

## Slide 5: Acknowledging previous work
American Megatrends / Lenovo SMM vulnerability (Sogeti ESEC)
CVE-2017-5689 in AMT (Maksim Malyutin, Embedi)
Intel ME Secrets (Igor Skochinsky, RECON 2014)
me_cleaner (Nicola Corna, many others)
Chris Tarnovsky’s work on TPMs (particularly DEFCON 20 talk)
[1] http://esec-lab.sogeti.com/posts/2016/05/30/smm-unchecked-pointer-vulnerability.html
[2] https://www.embedi.com/news/mythbusters-cve-2017-5689
[3] https://recon.cx/2014/slides/Recon%202014%20Skochinsky.pdf
[4] https://github.com/corna/me_cleaner
[5] https://www.youtube.com/watch?v=Bp26rPw90Dc

## Slide 6: Read your chipset datasheet
Chipset is a consumer colloquialism for what Intel calls the Platform Controller Hub (PCH)
Yes, you can just download the datasheet.
  Free!
  No account needed!
Contains all the useful things:
  Pinout, signal names, voltage levels
  Feature descriptions, configuration registers
  Architectural diagrams, implementation notes

## Slide 7: This sounds crazy!
It’s actually not that hard.
Little domain-specific knowledge required.
Ask people for help when you’re confused.
  Twitter
  IRC (Freenode #libreboot & #coreboot were a great help)

## Slide 8: Section 1: Messing with IME

## Slide 9: Rationale
Always running.
Has memory access.
Direct NIC access.
Closed platform.
No way to assess security.

## Slide 10: IME Debug Mode
Intel 7-Series (Z79/C600) Platform Controller Hub (PCH) Datasheet
Page 755, Section 22.1.2 “HSFS – Hardware Sequencing Flash Status Register”
Flash Descriptor Override Pin-Strap Status (FDOPSS)
“Read Only: This bit indicates the condition of the FDOPSS / Intel ME Debug Mode Pin-Strap.”
“The […] ME Debug Mode strap is set using external pull-up on HDA_SDO”
Notes: Chipset datasheet: https://www.intel.com/content/dam/www/public/us/en/documents/datasheets/7-series-chipset-pch-datasheet.pdf

## Slide 11: IME Debug Mode
Intel 7-Series (Z79/C600) Platform Controller Hub (PCH) Datasheet
Page 78, Table 2-26 “Functional Strap Definitions”
Notes: Chipset datasheet: https://www.intel.com/content/dam/www/public/us/en/documents/datasheets/7-series-chipset-pch-datasheet.pdf

## Slide 12: IME Debug Mode
Intel 7-Series (Z79/C600) Platform Controller Hub (PCH) Datasheet
Page 78, Table 2-26 “Functional Strap Definitions”
Notes: Chipset datasheet: https://www.intel.com/content/dam/www/public/us/en/documents/datasheets/7-series-chipset-pch-datasheet.pdf

## Slide 13: Posted findings
Tweets by @whitequark used with permission.
***

## Slide 14: What do we know?
HDA_SDO is the HD Audio Serial Data Out line.
  This is a physical wire from the PCH to the HDA codec IC.
  Unfortunately the PCH is a BGA part and it’s not an edge pin 
Pulling HDA_SDO low at boot puts IME into debug mode.
IME debug mode unlocks some registers.
Intel says it “must not be asserted”.
Notes: Chipset datasheet: https://www.intel.com/content/dam/www/public/us/en/documents/datasheets/c600-series-chipset-datasheet.pdf page 78

## Slide 15: What don't we know?
Aside from config registers, what does ME debug actually do?
Where can we access HDA_SDO?
What happens if we mess with those registers?

## Slide 16: Someone else to the rescue
Always look for prior research!
HDA_SDO strap already explored by libreboot/coreboot and me_cleaner folks
Stops IME from executing 
Breaks integrated GbE NIC 
Sets 30 minute shutdown timer 
Intel ME sectors are signed 

## Slide 17: Neutralising IME – option 1
Find HDA_SDO on board (HDA codec IC easiest)
Pull HDA_SDO to GND to assert ME Debug strap
Boot the system
Dump ME firmware flash from mapped memory
Neutralise with me_cleaner
Write neutralised image back to ME flash
Reboot

## Slide 18: Neutralising IME – option 2
Find ME flash device on board (8-pin SPI flash)
Desolder it or use IC clip
Use flashrom to dump the ME firmware flash
Neutralise with me_cleaner
Write neutralised image back to ME flash
Reboot
[1] https://hardenedlinux.github.io/firmware/2016/11/17/neutralize_ME_firmware_on_sandybridge_and_ivybridge.html

## Slide 19: me_cleaner approach
ME firmware is split into partitions
Partitions are signed (signature in partition header)
Image starts with Firmware Partition Table (FPT)
FPT itself is not signed!
Can just remove partitions (and headers containing signature) and this does not trigger the shutdown timer.
Only partition that cannot be removed is factory partition (FTPR)

## Slide 20: Problem
These modifications require you to touch hardware, and that sucks.

## Slide 21: Problem
No motherboard designer would expose IME straps in a way that we might abuse…

## Slide 22: Or would they? (Dell)
keyboard controller
Notes: Board schematics found online on laptop repair forums.

## Slide 23: Or would they? (Toshiba)
keyboard controller
Notes: Board schematics found online on laptop repair forums.

## Slide 24: Or would they? (Acer)
keyboard controller
Notes: Board schematics found online on laptop repair forums.

## Slide 25: Or would they?
Notes: Board info found online on laptop repair forums.

## Slide 26: Broken by specification
“Let’s expose HDA_SDO externally!”
Intel HD Audio specification
6.12 - Hot Attach Mechanisms
“An important feature for High Definition Audio is supporting hot attach. A typical example is connecting the Codec on the docking station.”

## Slide 27: Docking
Idea: assert ME Debug strap via docking connector on a laptop. No disassembly!
Reality: docking connectors are proprietary, change between laptop models, and aren’t documented.
Looked pretty hard, didn’t find anyone using hot attach on a docking connector 

## Slide 28: Future work
Identify and document convenient locations to interfere with IME (HDA_SDO pins, ME firmware flash IC) on various platforms.
Find a way to restore GbE NIC without ME access.

## Slide 29: Except…
Someone found a better way!

## Slide 30: HAP
High Availability Platform
Hidden flag to disable ME
Discovered by Mark Ermolov, Maxim Goryachy http://blog.ptsecurity.com/2017/08/disabling-intel-me.html
Released into me_cleaner in August 2017.
Still breaks GbE NIC in many cases though.

## Slide 31: Section 2: Architectural security issues

## Slide 32: Architectural security concerns
“Privileged” buses with non-privileged devices on them.
Security-critical devices (keyboard, TPM, NIC) sharing a bus with other devices.

## Slide 33: How do we find these?
Look at all the motherboards!
… expensive?
Leaked docs & right to repair ftw :D

## Slide 34: Why does my RAM have access to the NIC?
DIMM socket
LAN controller
Notes: Board schematic found on a laptop repair forum.

## Slide 35: Why does my RAM have access to the WiFi?
DIMM socket
WiFi SoC
Notes: Board schematic found on a laptop repair forum.

## Slide 36: New proposed concept
Internet of DIMMs

## Slide 37: Serial Presence Detect (SPD)
IC on DIMM used to store RAM config data
Talks via SMBus to PCH
Should be an SMBus slave device
SMBus is multimaster by design
What’s stopping it? (nothing)

## Slide 38: SPD
SPD IC == EEPROM
Common: ST M34xx, Microchip 34AAxx, Micron TN-04-42
Fairly ubiquitous pinout (3x address select, Vss, SDA, SCL, write control, VCC)
Coincidence: ATTiny85 has compatible pinout

## Slide 39: MCU as an SPD

## Slide 40: Approach
Replace SPD EEPROM with ATTiny85.
Use ATTiny85’s internal EEPROM for SPD data.
Interrupt-driven SMBus listener on PB0/PB1.
Evil mode: become SMBus master and send network packets via the IME.

## Slide 41: Status
Fake SPD working (contains normal SPD data)
SMBus Master code not complete (yet!)
Plan: magic value to SPD, sends packets
Worked out some of the NIC commands
Ongoing development, no demo yet 

## Slide 42: Section 3: Persistence

## Slide 43: Persisting outside HDD
UEFI/BIOS
IME firmware?
SMM?
Peripherals
RAM
Other motherboard ICs

## Slide 44: UEFI/BIOS
User-flashable
Updates are usually signed 
Data persistence possibly via empty config sections
Code persistence unlikely with SecureBoot
Likely requires targeted attack

## Slide 45: IME firmware
Physical access required to flash
Some regions OS-accessible (Intel Flash Descriptor)
Huffman coded but RE’ed (thanks to nico_h for this info!)
Potentially useful

## Slide 46: SMM
Not easily writable, as far as I know
Very hard to read even from ring0 (SMRAM)
People have done lots of research here, very new results suggest there may be ways to dump/write SMRAM

## Slide 47: Peripherals
Peripheral devices (GPU, NIC, SSD) with firmware
User-upgradeable from software
Variable checking of signatures
Potentially useful for storing secrets

## Slide 48: RAM
No, not the volatile bit.
SPD flash is read/write from kernel space
Known to be an exfiltration vector
Slack space & unused fields useful for secret storage
XSS via SPD flash (lol)

## Slide 49: Other motherboard ICs
PCH has volatile scratch registers
RAID controller firmware
Non-volatile flash space in sensors
Hard disk environmental logging

## Slide 50: Section 4: Secure Re-use

## Slide 51: Serious concerns
Modified firmware
Exploitation of firmware via modified data
Exfiltration / other contamination

## Slide 52: Secure re-use approach
Work with motherboard and peripheral vendors to identify devices with non-volatile storage
Dump the contents of these devices
Boot and use the system
Reflash the contents of the devices, verify writes and check stability
Store as known-good state
Restore before hardware crosses customer boundaries

## Slide 53: Challenges
Vendors may be unhelpful (e.g. HDD manufacturers get very cagey about you messing with the telemetry flash!)
Known-good state must be validated before customer use in the first place; this cannot be retroactive.
Laborious task. Requires staged reflashing and verification of writes + post-boot stability.
Potential failure state is permabricked hardware.
Loss or compromise of known-good states is catastrophic.

## Slide 54: Solutions
Good vendor relationships.
Early identification of risk. Invest early, plan appropriately.
Automation where possible. Hardware interface jigs help reduce manual effort.
Clear procedure and multiple validation and verification checks help eliminate potential bricking of hardware.
Secure & redundant storage of the states.

## Slide 55: Conclusions

## Slide 56: Conclusions
You should look at your hardware datasheets!
Board designs are very complex, so the potential for the designer to make mistakes is high.
Supply chain attacks don’t necessarily need to target security-critical devices.
Secure re-use of hardware is difficult.

## Slide 57: Special thanks
@whitequark
Tim Brown (@timb_machine)
Anonymous hardware security guy
nico_h and jn__ on #coreboot
Lots of people from #libreboot

## Slide 58: The end. Questions?